## Slide 1: Chapter 1 – Computer Systems

## Slide 2: CS 345
Stalling’s Chapter | # | Project
1: Computer System Overview 2: Operating System Overview | 4 | P1: Shell
3: Process Description and Control 4: Threads | 4 | P2: Tasking
5: Concurrency: ME and Synchronization 6: Concurrency: Deadlock and Starvation | 6 | P3: Jurassic Park
7: Memory Management 8: Virtual memory | 6 | P4: Virtual Memory
9: Uniprocessor Scheduling 10: Multiprocessor and Real-Time Scheduling | 6 | P5: Scheduling
11: I/O Management and Disk Scheduling 12: File Management | 8 | P6: FAT
Student Presentations | 6 | 

## Slide 3: Learning Objectives
Describe the basic elements of a computer system and their interrelationship.
Explain the steps taken by a processor to execute an instruction.
Understand the concept of interrupts and how and why a processor uses interrupts
List and describe the levels of a typical computer memory hierarchy.
Explain the basic characteristics of multiprocessor and multicore organization.
Discuss the concept of locality and analyze the performance of a multilevel memory hierarchy.
Understand the operation of a stack and its use to support procedure call and return.

## Slide 4
os345.c
os345interrupts.c
os345signals.c
os345tasks.c
os345semaphores.c
P1: Shell
os345p1.c
P2: Tasking
os345p2.c
P3: Jurassic Park
os345p3.c
os345park.c
P4: Virtual Memory
os345p4.c
os345mmu.c
os345lc3.c
P5: FSS Scheduling
os345p5.c
P6: FAT File Manager
os345p6.c
os345FAT.c
OS345
P1, P2
P1, P2, P5

## Slide 5: Learning Objectives
Describe the basic elements of a computer system and their interrelationship.
Explain the steps taken by a processor to execute an instruction.
Understand the concept of interrupts and how and why a processor uses interrupts
List and describe the levels of a typical computer memory hierarchy.
Explain the basic characteristics of multiprocessor and multicore organization.
Discuss the concept of locality and analyze the performance of a multilevel memory hierarchy.
Understand the operation of a stack and its use to support procedure call and return.

## Slide 6: Processor Registers
User-visible registers
  May be referenced by machine language
  Available to all programs - application programs and system programs
    Data Registers – can be changed by user
    Address Registers – could be separate from data register
    Stack Registers – user / supervisor stacks
    Condition Codes – results of operations
Control and status registers
  May or may not be visible
    Program Counter (PC) – address of next instruction
    Instruction Register (IR) – most recently fetched instruction
    MAR/MBR – memory reference registers
    Program Status Word (PSW) – condition codes, interrupts, mode
Registers

## Slide 7: CPU
Registers

## Slide 8: Instruction Execution
Registers

## Slide 9: Instruction Execution
Registers

## Slide 10: Learning Objectives
Describe the basic elements of a computer system and their interrelationship.
Explain the steps taken by a processor to execute an instruction.
Understand the concept of interrupts and how and why a processor uses interrupts
List and describe the levels of a typical computer memory hierarchy.
Explain the basic characteristics of multiprocessor and multicore organization.
Discuss the concept of locality and analyze the performance of a multilevel memory hierarchy.
Understand the operation of a stack and its use to support procedure call and return.

## Slide 11: Interrupt Service Routines
Main Routine
(synchronous)
Interrupt Service Routine
Interrupt
Interrupt Service Routine
(asynchronous)
Main Routine
(synchronous)
Interrupt Service Routine
(asynchronous)
Main Routine
(synchronous)
Interrupt Service Routine
(asynchronous)
Main Routine
(synchronous)

## Slide 12: Interrupts
The interrupt was the principle tool available to system programmers in developing multi-tasking systems!
Classes of Interrupts
  Program: arithmetic overflow, division by zero
  Execute illegal instruction
  Reference outside user’s memory space
  I/O: Timer, DMA
  Hardware failure
Interrupt control
  Disable during ISR
  Enable upon exiting
  Allow Interrupts?
  Priorities?

## Slide 13: Learning Objectives
Describe the basic elements of a computer system and their interrelationship.
Explain the steps taken by a processor to execute an instruction.
Understand the concept of interrupts and how and why a processor uses interrupts
List and describe the levels of a typical computer memory hierarchy.
Explain the basic characteristics of multiprocessor and multicore organization.
Discuss the concept of locality and analyze the performance of a multilevel memory hierarchy.
Understand the operation of a stack and its use to support procedure call and return.

## Slide 14: Storage Performance
Level | 1
Name | Registers
Typical Size | < 1KB
Implementation Technology | Custom memory w/multiple ports CMOS
Access time (ns) | 0.25-0.5
Bandwidth (MB/sec) | 20,000-100,000
Managed by | Compiler
Backed by | Cache

## Slide 15: Storage Performance
Level | 1 | 2
Name | Registers | Cache
Typical Size | < 1KB | < 16MB
Implementation Technology | Custom memory w/multiple ports CMOS | On-chip CMOS RAM
Access time (ns) | 0.25-0.5 | 0.5-25
Bandwidth (MB/sec) | 20,000-100,000 | 5,000-10,000
Managed by | Compiler | Hardware
Backed by | Cache | Main

## Slide 16: Storage Performance
Level | 1 | 2 | 3
Name | Registers | Cache | Main memory
Typical Size | < 1KB | < 16MB | <64GB
Implementation Technology | Custom memory w/multiple ports CMOS | On-chip CMOS RAM | CMOS SRAM
Access time (ns) | 0.25-0.5 | 0.5-25 | 80-250
Bandwidth (MB/sec) | 20,000-100,000 | 5,000-10,000 | 1,000-5,000
Managed by | Compiler | Hardware | OS
Backed by | Cache | Main | Disk

## Slide 17: Storage Performance
Level | 1 | 2 | 3 | 4
Name | Registers | Cache | Main memory | Solid state disk
Typical Size | < 1KB | < 16MB | <64GB | <1TB
Implementation Technology | Custom memory w/multiple ports CMOS | On-chip CMOS RAM | CMOS SRAM | Flash
Access time (ns) | 0.25-0.5 | 0.5-25 | 80-250 | 25,000-50,000
Bandwidth (MB/sec) | 20,000-100,000 | 5,000-10,000 | 1,000-5,000 | 500
Managed by | Compiler | Hardware | OS | OS
Backed by | Cache | Main | Disk | Disk

## Slide 18: Storage Performance
Level | 1 | 2 | 3 | 4 | 5
Name | Registers | Cache | Main memory | Solid state disk | Hard disk
Typical Size | < 1KB | < 16MB | <64GB | <1TB | <10TB
Implementation Technology | Custom memory w/multiple ports CMOS | On-chip CMOS RAM | CMOS SRAM | Flash | Hard disk
Access time (ns) | 0.25-0.5 | 0.5-25 | 80-250 | 25,000-50,000 | 5,000,000
Bandwidth (MB/sec) | 20,000-100,000 | 5,000-10,000 | 1,000-5,000 | 500 | 20-50
Managed by | Compiler | Hardware | OS | OS | OS
Backed by | Cache | Main | Disk | Disk | Disk or tape

## Slide 19: Learning Objectives
Describe the basic elements of a computer system and their interrelationship.
Explain the steps taken by a processor to execute an instruction.
Understand the concept of interrupts and how and why a processor uses interrupts
List and describe the levels of a typical computer memory hierarchy.
Explain the basic characteristics of multiprocessor and multicore organization.
Discuss the concept of locality and analyze the performance of a multilevel memory hierarchy.
Understand the operation of a stack and its use to support procedure call and return.

## Slide 20: Multi (processor/core)
  Cluster computing
    Loosely coupled - network
    Client / server environment
    Middleware
    DME, RPC
Traditionally, the computer has been viewed as a sequential machine.
  Multiple control signals
  Pipelining
Parallelism
  Symmetric Multiprocessors (SMP)
    2 or more identical processors that share resources
    Integrated OS to control jobs, tasks, files, data elements…
    High degree of interaction/cooperation between processes
  Multicore Computers
    Single piece of silicon (die)
    Independent processors + levels of cache
    Intel Core i7
    Prefetching

## Slide 21: Learning Objectives
Describe the basic elements of a computer system and their interrelationship.
Explain the steps taken by a processor to execute an instruction.
Understand the concept of interrupts and how and why a processor uses interrupts
List and describe the levels of a typical computer memory hierarchy.
Explain the basic characteristics of multiprocessor and multicore organization.
Discuss the concept of locality and analyze the performance of a multilevel memory hierarchy.
Understand the operation of a stack and its use to support procedure call and return.

## Slide 22
Given:
  Processor speed is faster than memory speed
  Execution/data localizes
Processor Cache:
  Contains a portion of main memory
  Invisible to operating system
  Used similar to virtual memory
  Increases the speed of memory
Processor first checks cache - If not found in cache, the block of memory containing the needed information is moved to the cache
Disk cache, I/O cache, VM cache,…

## Slide 23: Two-Level Memory
Locality
  Spatial locality – clustered access
    Large cache
    Pre-fetch
  Temporal locality – recent/repeated access
    Cache Least Recently Used (LRU)
    Cache hierarchy

## Slide 24: Learning Objectives
Describe the basic elements of a computer system and their interrelationship.
Explain the steps taken by a processor to execute an instruction.
Understand the concept of interrupts and how and why a processor uses interrupts
List and describe the levels of a typical computer memory hierarchy.
Explain the basic characteristics of multiprocessor and multicore organization.
Discuss the concept of locality and analyze the performance of a multilevel memory hierarchy.
Understand the operation of a stack and its use to support procedure call and return.

## Slide 25: The Call / Return Mechanism
Subroutines
Smaller programs.
Easier to maintain.
Reduces development costs.
Increased reliability.
Fewer bugs do to copying code.
More library friendly.
Faster programs.
Less overhead.

## Slide 27: Summary…

## Slide 28: What is an O.S.?
Not always a clear definition as to what constitutes an O.S. and what is an application
  CD-Rom Driver
  Scandisk
  Internet Explorer
Intermediary between the hardware and the users
  Allocate resources (CPU, Memory, disk space, etc.) between programs and users efficiently
  Allow the user to conveniently access data and programs
  Protect the system from incorrect or malicious programs and users
Summary

## Slide 29: Hardware Review
Elements of a system:
  Processor
    Registers (address, data, control)
    Instruction cycle (fetch, decode, execute)
    Interrupts
    Usually includes hardware and special instructions to help the O.S. manage memory, devices, etc.
  Memory
    Different levels (cache, main memory, disk)
    Operating system will generally manage memory (both RAM and disk), and move data back and forth as required
  I/O
    Usually use Interrupts, DMA
    Operating system usually controls use of I/O devices
Summary

## Slide 30: Registers
Used for frequently accessed items
User-Visible registers – Available to the programmer and compiler
  Data Registers
  Address Registers (Index, Segment, Stack Pointer)
  Condition code/flags
Control and Status registers – Used to control the processor
  Program Counter/Instruction Pointer
  Memory address/data
  Processor Status Word
  Debugging registers
  Temp registers
  Memory Management registers
Summary

## Slide 31: Interrupts
Interrupts
  Allow I/O devices to get the CPUs attention at regular intervals (Program, Timer, I/O, Hardware failure)
  Helps the O.S. by reducing the time spent monitoring I/O devices
  CPU checks for interrupts after each instruction, starts the handler if needed
  May allow nested interrupts
I/O techniques
  Programmed I/O
  Interrupt-Driven I/O
  Direct Memory Access
Summary

## Slide 32: Interrupts and I/O
Handling and Interrupts:
  Figure 1.10 (pg 23)
  Device sends interrupt request to CPU
  CPU finishes current instruction
  CPU acknowledges request
  CPU saves PC and PSW
  CPU loads PC with the address of the first instruction in the interrupt handler (may get help from interrupt request)
  Interrupt handler starts, often saves other CPU registers and key values
  Interrupt handler responds to the device
  Interrupt handler restores CPU registers and key values
  CPU restores PC and PSW and resumes previous program
Summary

## Slide 33: Memory
Varying types of memory
  Registers, Cache, RAM, Disk, CD
  Vary in speed, size, cost
  CPU and O.S. try to keep frequently used data in faster memory
Cache – Use a small high-speed memory to improve the apparent speed of a larger low-speed memory
  Keep track of what is currently being used, load into high-speed memory
  Replacement Algorithm – What do we get rid of when we run out of memory?
  Write Policy – How do we respond to modifications?
Summary

## Slide 34: Finally…
Operating System Tradeoffs
  Convenience vs efficiency
  Ease of use vs maximum resource utilization
  Interactive user interface vs no user view
  Asymmetric vs symmetric processing
  Single-processor vs multiprocessor systems
  Unicore vs multicore systems
  UMA vs NUMA
  Batch vs time sharing
  Logical vs physical memory
  Dual mode vs multimode
Notes: UMA = uniform memory access
Non-uniform memory access (NUMA) is a computer memory design used in multiprocessing, where the memory access time depends on the memory location relative to the processor. Under NUMA, a processor can access its own local memory faster than non-local memory (memory local to another processor or memory shared between processors). The benefits of NUMA are limited to particular workloads, notably on servers where the data are often associated strongly with certain tasks or users.[